## Slide 1
Mapping GADS (Generation)
and TADS (Transmission)
Using Velocity Suite for Extreme Weather Resiliency Planning
Aryan Ritwajeet Jha
Intern for Summer 2024
Assisting Svetlana Ekisheva and Christopher Claypool
as part of
Advanced System Analytics & Modelling (ASAM)
NERC

## Slide 2: Objective for Mapping GADS and TADS
We wish to identify the transmission lines and generators most susceptible to extreme weather events
Doing so would enable us to make better planning recommendations to Transmission Owners (TOs) and Generator Owners (GOs).
Example: Mapping Energy Infrastructure Risk in Florida.
Retrieved from Prof. Thrall’s YouTube Video
Billion Dollar Weather Climate Disasters
Image from Unison Energy

## Slide 3: Objective for Mapping GADS and TADS
NERC has data on Bulk Power System (BPS) components including Transmission Lines (via [TADS]) and Generators (via [GADS])
By Mapping these BPS components to their geographical location we have knowledge of weather events and climate data near those locations.
Transmission Data
Geographical Mapping (Weather)
Generator Data
Extreme Weather Resiliency Studies
GADS: Generating Availability Data System
TADS: Transmission Availability Data System

## Slide 4: Objective for Mapping GADS and TADS
With the weather data near those BPS components, we can then determine if any outages were primarily caused due to extreme weather events.
A study correlating the extreme weather around a BPS component to the outages could be done, on similar lines as [ekisheva2024, ekisheva2023]
TADS:
Transmission Line retired that day
Local Weather:
Exceptionally high winds that day
TADS:
Generator taken off the grid that day
Local Weather:
Heavy blizzard that day
Reality (correlated)
Reality (correlated)

## Slide 5
The Problem at Hand
Generator Units
Transmission Lines
Geographical Mapping
Weather Data
Missing Link!
From GADS
From TADS
From Weather Stations

## Slide 6
The Workaround: Using Velocity Suite
Generator Units
Transmission Lines
Geographical Mapping
Weather Data
From GADS
From TADS
From Velocity Suite
Generator Units
Transmission Lines
From Velocity Suite, get a list of components which are already close to a particular weather station.
This way, both component data and its mapping is taken care of in one go.
Since geographical data is not collected in GADS/TADS, the generators/transmission lines are being indirectly mapped using Velocity Suite [VelocitySuite]

## Slide 7
The Resulting Problem at Hand:
How to Match Components between the Two Databases?
Generator Units
Transmission Lines
From GADS
From TADS
Geographical Mapping
Weather Data
From Velocity Suite
Generator Units
Transmission Lines
Many discrepancies in reporting of data between the two databases!
TADS/GADS | Velocity Suite
Huge, Singular Database ( Entries in TADS) | Smaller, Location-specific Database ( Entries per Location)
Usually has a minimum cutoff (say, MW Rating) for reporting of component | Many results irrelevant to GADS/TADS
"Commonwealth Edison Co“ in Company Name | "Commonwealth Edison Company"
“eia336” in EIA Code | “00336”
From Bus: A, To Bus: B | From Bus: B, To Bus: C From Bus: C, To Bus: A
TADS/GADS | Velocity Suite
Usually has a minimum cutoff (say, MW Rating) for reporting of component | Many results irrelevant to GADS/TADS
"Commonwealth Edison Co“ in Company Name | "Commonwealth Edison Company"
“eia336” in EIA Code | “00336”
From Bus: A, To Bus: B | From Bus: B, To Bus: C From Bus: C, To Bus: A

## Slide 8
API Calls are made to Velocity Suite along the lines of:
“List and Map all Transmission Lines which are <specific distance> from <specific weather station>*”
which will then output the qualifying transmission lines on a map and can export the TO data as an excel file.
Workflow
An API Call for Transmission Lines rated higher than 100kV which are within 50 miles of Chicago O'Hare Weather Station
An API Call for Generator Plants which are within 50 miles of Chicago O'Hare Weather Station
* Weather Stations at Airports are ideal for extreme weather studies as they have the most granularity when it comes to time-series measurements related to the weather
Similarly, output if the API Call was made for Generator Units instead

## Slide 9
Python scripts parse the excel files from Velocity Suite, as well as GADS/TADS and attempt to make ‘matches’ (i.e. the same component represented by both GADS/TADS and Velocity Suite) based on various heuristics.
If a ‘match’ is ascertained, the Rec_ID from Velocity Suite is ‘attached’ to the GADS/TADS data, so that for future cases, we have an approximate geographical location (nearest weather station) of that BPS components
Workflow:
Key Columns to Match
Generator Units
Transmission Lines
From GADS
From TADS
Geographical Mapping
Weather Data
From Velocity Suite
Generator Units
Transmission Lines
Rec_ID
Rec_ID
Rec_ID
EIA Code
EIA Code
FromBus, ToBus
Company Name
Plant Name
kV Rating
FromBus, ToBus
Company Name
kV Rating
Plant Name
State
State

## Slide 10
High-level Workflow for Mapping GADS
via Velocity Suite Generator Plants
Parse Velocity Suite Data (Generator Plants)
Ascertain US States
Remove entries without EIA Codes [eia]
Parse GADS Data
Filter based on the US States from Velocity Suite
Remove entries without EIA Codes
Create a Table of Matches
Match between GADS and VS based on same EIA Code values
Attach the `Rec_ID` from VS into the table.
Now we have a table of generators whose geographical location we know
Data | 
Generator Plants from GADS mapped** | 25
Generator Units from GADS mapped | 126
*Entries in GADS are Generator Units, which are only associated with Generator Plants having a combined** rating of . Most Generator Plants from Velocity Suite are smaller (typically ) and thus may not be matched with any entry in GADS.
Location 1: Chicago O’Hare
** Combined Rating here is taken as the sum of Cancelled/Mothballed/Operating/Planned/Retired Cap MW ratings. Several plants have been found to have their only non-zero values in the Cancelled/Retired categories (i.e. they are basically out of operation).
Performing the same analysis for a different location is as easy as changing a single line of code.
Data | 
Generator Plants from GADS mapped** | 66
Generator Units from GADS mapped | 266
Location 2: New York JFK

## Slide 11
High-level Workflow for Mapping GADS
via Velocity Suite Generator Units
Parse Velocity Suite Data (Generator Plants)
Ascertain US States
Remove entries without EIA Codes [eia]
Parse GADS Data
Filter based on the US States from Velocity Suite
Remove entries without EIA Codes
Create a Table of Matches
Match between GADS and VS Units based on same EIA Code values
Attach the Rec_ID from VS into the table.
Now we have a table of generators whose geographical location we know
Parse Velocity Suite Data (Generator Units)
Match Plant Names between VS Plants and VS Units
Map the EIA and Rec_ID entries from VS Plants onto the VS Units
On similar lines as the Generator Plants from Velocity Suite, Generator Units from Velocity Suite were also matched with the GADS Units, with some small adjustments in the workflow, and identical results were obtained.

## Slide 12
High-level Workflow for Mapping TADS
via Velocity Suite Transmission Lines
Parse Velocity Suite Data (Transmission Lines)
Ascertain Company Names
Parse TADS Data (Transmission Lines)
(Ideally) Filter based on the Company Names from Velocity Suite
Create a Table of Matches
Match between TADS and VS based on same unordered pair of (fromBus, toBus)
Attach the `Rec_ID` from VS into the table.
Now we have a table of transmission lines whose geographical location we know
Filter transmission lines below rating of
Filter transmission lines below rating of 100𝑘𝑉
Parse Velocity Suite Data (Transmission Lines)
Parse TADS Data (Transmission Lines)
(Ideally) Filter based on the Company Names from Velocity Suite
Create a Table of Matches
Match between TADS and VS based on same unordered pair of (fromBus, toBus)
Attach the `Rec_ID` from VS into the table.
Now we have a table of transmission lines whose geographical location we know
Data | 
Transmission Lines from TADS mapped** | 127
Entries in TADS are for transmission lines rated at a voltage .
Location 1: Chicago O’Hare
** Mapping was done based on exactly matching unordered (fromBus, toBus) tuples. Many potential matches were lost because of inconsistent naming of transmission lines and even operating companies between the two databases. Overall careful manual labour (in mapping company names and bus names) required for mapping more TADS transmission lines.
Location 2: New York JFK
Data | 
Transmission Lines from TADS mapped** | 111

## Slide 13: Summary and Future Work: Automated the process of mapping BPS components. The output can now be used for extreme weather resiliency analysis when coupled with weather data. A little manual effort (such as ensuring consistency in company names) goes a long way in the analysis. So far only ‘exact’ matches were made. Future work could include making inexact, ‘fuzzy’ matches to capture potential matches left out due to data entry inaccuracies. If GADS/TADS data collection could also include some sort of approximate geographical index, it would greatly assist in this analysis.

## Slide 14
The codebase including input and output excel files may be found in the NERC Staff Directory: H:\Mapping\Aryan
Have Git Bash [GitBash] installed (for running terminal commands)
Navigate to the directory H:\Mapping\Aryan\extreme-weather-repo-FOR-END-USERS
Open Git Bash in the directory (<Right Click in the directory> -> Open Git Bash here)
Workflow
Repo Handling if You Prefer Version Control like GitHub
2
3

## Slide 15
Run the command: git reset --hard && git clean -fd && git pull origin master
After several minutes*, your directory is now up to date with the latest uploaded changes (Note that the actual directory with all the changes is the ‘bare’ repository extreme-weather-repo, even if it may look mostly empty). Running the command ‘extracts’ the contents of extreme-weather-repo into extreme-weather-repo-FOR-END-USERS
Workflow
Repo Handling if You Prefer Version Control like GitHub
4
* It takes that long because of NERC VPN.

## Slide 16
[TADS] Transmission Availability Data System (TADS). (2024, June 17). Retrieved from https://www.nerc.com/pa/RAPA/tads/Pages/default.aspx
[GADS] Generating Availability Data System (GADS). (2024, August 07). Retrieved from https://www.nerc.com/pa/RAPA/gads/Pages/GeneratingAvailabilityDataSystem-(GADS).aspx
[ekisheva2024] Svetlana Ekisheva, Christopher Claypool, Marilyn Jayachandran, Mark G. Lauby, Weather resilience of transmission system in Florida measured and tracked with detailed outage and weather data, the 18th International conference on Probabilistic Methods Applied to Power Systems (PMAPS), 2024 (to be published).
‪[ekisheva2023] Ekisheva, S., Pratt, D. K., Kachadurian, M., Martin, W. G., Norris, J., & Dobson, I. . Grid Restoration After Extreme Weather Events. 2023 IEEE PES Innovative Smart Grid Technologies Europe (ISGT EUROPE). IEEE. doi: 10.1109/ISGTEUROPE56780.2023.10407350
[VelocitySuite] Velocity Suite: The premier analytical source for energy information. (2024, January 22). Retrieved from https://www.hitachienergy.com/us/en/products-and-solutions/energy-portfolio-management/market-intelligence-services/velocity-suite
References

## Slide 17
[GitBash] Git - Downloading Package. (2024, August 07). Retrieved from https://git-scm.com/download/win
[eia] Homepage - U.S. Energy Information Administration (EIA). (2024, August 07). Retrieved from https://www.eia.gov
References

## Slide 18
Questions and Answers