## Slide 1: Scalable Multi-Period Optimal Power Flow for Active Power Distribution Systems or simply, Scalable MP-OPF in ADS
Aryan Ritwajeet Jha
Graduate Research Assistant
Washington State University
Notes: Remember to hit the reset button to make sure all the page elements react properly.
There are 20 different layouts that you can choose from.

## Slide 2: Dual Variables Comparison Terminal SOC Constraint Relaxed
All batteries: values for all batteries for any particular time step are pretty much the same, and strongly correlated with the Substation Power Cost
DDP value for is weirdly positive (similar magnitude as other timesteps), even though every other in the horizon in DDP as well as every in BF are all negative.
Note: It itself is not used in DDP workflow.
BruteForced (BF)
BruteForced (BF)

## Slide 3: Dual Variables Comparison Terminal SOC Constraint Relaxed
BruteForced (BF)
All batteries: values for all batteries for any particular time step are pretty much the same, and strongly correlated with the Substation Power Cost
BruteForced (BF)
DDP value for is weirdly positive (similar magnitude as other timesteps), even though every other in the horizon in DDP as well as every in BF are all negative.
Note: It itself is not used in DDP workflow.

## Slide 4: Dual Variables Comparison Terminal SOC Constraint Enforced
All batteries: values for all batteries for any particular time step are pretty much the same, and strongly correlated with the Substation Power Cost
DDP value for is weirdly positive (similar magnitude as other timesteps), even though every other in the horizon in DDP as well as every in BF are all negative.
Note: It itself is not used in DDP workflow.
BruteForced (BF)
BruteForced (BF)

## Slide 5: Dual Variables Comparison Terminal SOC Constraint Enforced
BruteForced (BF)
All batteries: values for all batteries for any particular time step are pretty much the same, and strongly correlated with the Substation Power Cost
BruteForced (BF)
DDP value for is weirdly positive (similar magnitude as other timesteps), even though every other in the horizon in DDP as well as every in BF are all negative.
Note: It itself is not used in DDP workflow.

## Slide 6: DDP Codebase Workflow
Parser
Optimizer
Post-processing and Validation

## Slide 7: DDP Codebase Workflow
Model Building
Model Solving

## Slide 8: DDP Codebase Workflow
Model Building
Model Solving

## Slide 9: DDP Codebase Workflow
Model Copied from
Model Altered as per this iteration:
  Objective function of model updated with latest available Model Solving

## Slide 10: IEEE_ph: MPCOPF Run for
MPCOPF Simulation Results
OpenDSS Powerflow Results
Timings
OpenDSS Def Profiles
Substation Power Cost
Objective
Objective
Miscomputation - will be fixed later
Discrepancies

## Slide 11: IEEE_ph: MPCOPF Run for
OpenDSS Def Profiles
Substation Power Cost

## Slide 12: IEEE_ph: MPCOPF Run for
OpenDSS Def Profiles
Substation Power Cost
IpOpt
Juniper
Minor difference between solver optimal decision variables

## Slide 13: Three Steps for Optimization Implementation (and what will be different for DDP):
  [No change] Loading Simulation Configuration from OpenDSS (.dss) files, Pre-optimization housekeeping
  [Some change] Optimization Routine (Temporally brute forced optimization now verified, can be used as ‘Benchmark’ result for checking Optimality Gap)
  [No change] Post Optimization result validation via OpenDSSDirect
Initial Test System: ADS_ph with Loads, PVs and Batteries
Now onto writing the script for DDP optimization routine ..

## Slide 14: Latest Slides End Here. Previous Slides Follow.

## Slide 15: IEEE_ph: MPCOPF Run for
MPCOPF Simulation Results
OpenDSS Powerflow Results
Timings
OpenDSS Def Profiles
Substation Power Cost
Objective
Objective
Miscomputation - will be fixed later
Discrepancies
Weirdly high discrepancy in voltage (will be investigated)

## Slide 16: IEEE_ph: MPCOPF Run for
OpenDSS Def Profiles
Substation Power Cost

## Slide 17: ADS_ph: MPCOPF Run for
MPCOPF Simulation Results
OpenDSS Powerflow Results
Timings
OpenDSS Def Profiles
Substation Power Cost
Objective
Discrepancies
Objective
Miscomputation - will be fixed later

## Slide 18: ADS_ph: MPCOPF Run for
OpenDSS Def Profiles
Substation Power Cost

## Slide 19: DDP for MPOPF for ADS Workflow

## Slide 20: DDP for MPOPF for ADS Workflow

## Slide 21: Steps towards understanding Temporal Decomposition – Which Papers to Read?
Find work where it has actually been used.
  Beginning with only those which solve for the MPOPF problem.
    Right now, Transmission systems are OK too (they have to deal with ramping up/down constraints for generators)
    But may look into other domains as well afterwards
  Ascertaining which approach to follow, based on certain desirable features the future algorithm should have.

## Slide 22: Steps towards understanding Temporal Decomposition – Intended Algorithmic Solution
  Desirable features the future algorithm should have:
    Should be scalable with respect to Time (horizon duration)
      At least, something like time-steps should be solvable in one go
    Should ideally solve for the ‘true’ nonlinear problem, with as few approximations as possible
    Relaxations however are fine, and if they’re used, their solutions will obviously be checked for any infeasibility.
    Changing optimization formulation is undesirable for me. Something close to, if not exactly the same as the ‘standard’ nonlinear Branch Flow Model [farivar2013] is what I want.
      So, I’m looking to solve the problem using Branch Flow Variables only.
      Many papers, bring out their own new set of variables, approximations, customized algorithms to deal with them, in order to solve for the MPOPF problem. This is NOT what I’m looking to do.

## Slide 23: Do others ‘scalably’ solve MPOPF? – Some of them, Yes.
  These days, many papers pose a solution to the MPOPF problem.
    Many papers don't actually solve the problem in a scalable manner: the test-cases are reasonable (moderate sized, moderate penetration, day-ahead or large sized, low penetration, some hours only), but even they acknowledge that this formulation is not scalable, unless ...
    … Approximations are made

## Slide 24: How do others ‘scalably’ solve it? – Linearized Solution, Iteratively Improved
    Specifically,
    … Approximations are made at the most modular form of OPF formulation [usman2022, usman2023] which itself could be within a loop, where some meta-parameters are adjusted based on successive iterative updates.
      Some papers model these successive iterative updates on a homotopy based paradigm [agarwal2022]
MILP call inside a bigger algorithm
Some homotopy thing

## Slide 25: How do others ‘scalably’ solve it? – Hierarchical Optimization, Approximated (Relaxed) Top Level Step
    Specifically,
    The full optimization problem is divided into hierarchies, with the top hierarchy problem solving for an approximate (relaxed) model of the full horizon MINLP (NLP) problem.
    Once the top-level problem is solved and set-points for temporally-coupling decision variables are obtained, the same decision variables are kept as constant for every single time-step’s OPF formulation.
    The now temporally-decoupled Single-Period Optimal Power Flow Problems are formulated as SOCP (NLP) in a parallel manner.
    [nazir2018 (nazir2020)]
Inner SOCP call within an outer MILP loop
Inner NLP call within an outer SOCP loop

## Slide 26: How do others ‘scalably’ solve it? – Some sort of Algorithms involving Primal Dual Decomposition of the Constraints containing Variables from different time-steps
  Not fully appreciated (understood) by me yet. But here are two instances:
  In [agarwal2022] Their transmission system has many kinds of constraints, but only two temporally coupling constraints – Generator Ramping (one upper bound inequality and one lower bound inequality for each generator for each ‘time-boundary’) and Battery SOC (one equality for each battery for each time-boundary). All other equality/inequality constraints are constraints within a particular time-step, and thus are also called as uncoupled constraints.
  They then formulate a Lagrangian Function for the full OPF problem. After grouping ‘like’ terms together (as in whether they are temporally coupled or uncoupled), they ended up with this equation, which has (a summation of) temporally coupled terms (which come arise from the three kinds of temporal constraints) and temporally uncoupled terms (all contained in the first term)
  Finally, from the full horizon problem, a -th time-step problem function is carved out, which, outside the variables for that time-step, only contains certain primal and dual variables outside the time-step, including:
    (both lower and upper bounds),
Generator Ramping Constraints
Battery SOC Constraint
Lagrangian Function representing the full MPOPF problem (all time-steps)
Lagrangian Function representing the OPF problem for the -th time-step. Notice that the ‘new’ blocks are just terms from the ‘existing’ blocks but coming from the adjacent time-steps to

## Slide 27: How do others ‘scalably’ solve it? – Some sort of Algorithms involving Primal Dual Decomposition of the Constraints containing Variables from different time-steps
  Finally, from the full horizon problem, a -th time-step problem function is carved out, which, outside the variables for that time-step, only contains certain primal and dual variables outside the time-step, including:
    Past Primal Variables:
    Future Dual Variables: (both lower and upper bounds),
    While the problem itself cannot be solved for without knowing both past and future variables, as part of their Differential Dynamic Programming (DDP) Paradigm, they do a Forwards Pass and a Backwards Pass, wherein in each pass, they assume one set of variables to be constant (initially guessed, or possibly known from a previous computation).
Lagrangian Function representing the OPF problem for the -th time-step.

## Slide 28: How do others ‘scalably’ solve it? – Some sort of Algorithms involving Primal Dual Decomposition of the Constraints containing Variables from different time-steps
      Past Primal Variables:
      Future Dual Variables: (both lower and upper bounds),
    Specifically, in Forward Pass, they use the solved-for values of the past primal variables i.e. from the -th step as knowns for the problem at the -th step, and assume the last-known/initially-guessed values of the dual variables from the future i.e. from the -th step as constants, in order to fully solve the problem at the -th step.
    Once the values of the primal variables values for the -th step is known, they proceed one step forward, this time using those as the values of the past primal variables, again assuming the future dual variables as some constants.
    This forward pass process continues till the end-of-horizon (last time-step, let’s call it ).
Lagrangian Function representing the OPF problem for the -th time-step.
Scheme for Forward Pass and Backward Pass (here called ‘Sweep’ with no difference)

## Slide 29: How do others ‘scalably’ solve it? – Some sort of Algorithms involving Primal Dual Decomposition of the Constraints containing Variables from different time-steps
      Past Primal Variables:
      Future Dual Variables: (both lower and upper bounds),
  Once a forward pass is completed, i.e. the cost of the forward trajectory is constructed. It is time to solve for the gradients that will update the dual variables for the next forward pass.
  Thus after computation of these gradients, the next set of dual variables is computed.
  The process of Forward Pass and Backward Pass updates is carried on until convergence is achieved (updates no longer being significant).
Equations used for updating the future dual variables as part of the Backward Pass
Lagrangian Function representing the OPF problem for the -th time-step.
Scheme for Forward Pass and Backward Pass (here called ‘Sweep’ with no difference)

## Slide 30: How do others ‘scalably’ solve it? – Some sort of Algorithms involving Primal Dual Decomposition of the Constraints containing Variables from different time-steps
  Thus after computation of these gradients, the next set of dual variables is computed.
  The process of Forward Pass and Backward Pass updates is carried on until convergence is achieved (updates no longer being significant).
Done: I’ve understood the overall structure of a DDP implementation. Specifically, I’ve understood what is known, what is solved for, and what is assumed constant within a single time-period’s OPF. I understand the ‘Forward Pass’ component.
Current: I’m still studying the derivation required to understand the ‘Backward-Pass’ (how to use the gradient of the Lagrangian to get the dual variable updates). Once that is understood, I’ll have the understanding of one way to temporally decouple MPOPF for my use-case (ADS) as well, in a manner which can be implemented in code.
Equations used for updating the future dual variables as part of the Backward Pass
Lagrangian Function representing the OPF problem for the -th time-step.
Scheme for Forward Pass and Backward Pass (here called ‘Sweep’ with no difference)

## Slide 31: How do others ‘scalably’ solve it? – Some sort of Algorithms involving Primal Dual Decomposition of the Constraints containing Variables from different time-steps
  A paper utilizing ADMM for temporal decomposition: [pinto2020]
  Deficiencies:
    I don’t understand how ADMM works, because I don’t understand how dual variables work.
    To have a good understanding of dual variables, I have been reading up on theory [wolf2011]. I’ve gained some confidence in it but am yet to understand certain other key concepts thoroughly.
  The plan is to understand dual variables [wolf2011]., understand ADMM, understand ADMM usage in OPF [peng2015] , ultimately understand ADMM in MPOPF [pinto2020]
  .