## Slide 1: Spatially Distributed Multi Period Optimal Power Flow with Battery Energy Storage Systems
Aryan Ritwajeet Jha, Graduate Research Assistant1
Subho Paul, Assistant Professor2
Anamika Dubey, Associate Professor1
1 Energy Systems Innovation Center, School of Electrical Engineering and Computer Science, Voiland College of Engineering, Washington State University, Pullman, WA, USA
2 Department of Electrical Engineering, Indian Institute of Technology (BHU) Varanasi, Varanasi, UP, India
Notes: Remember to hit the reset button to make sure all the page elements react properly.
There are 20 different layouts that you can choose from.

## Slide 2: Quick Overview of the contents of this presentation
A comparison of Spatially Decomposed MPDOPF results vs the Centralized MPCOPF algorithm
Example describing spatial decomposition of the OPF problem (DOPF), and extension to MPDOPF.
Quick overview of the modelling of the optimization problem
Brief describing a standard OPF problem for Distribution Systems and MPOPF problem.

## Slide 3: OPF, MPOPF, Scalability of the problem

## Slide 4: The Optimal Power Flow (OPF) problem for Active Distribution Systems
Desired Objective Function
Network Constraints
Engineering Constraints
Component Constraints (DERs, Batteries)
Optimal?
Feasible?
Substation
Power
Loads and Controllable/Uncontrollable Components spread across a topology

## Slide 5: The Multi Period Optimal Power Flow (MPOPF) problem for Active Distribution Systems
Intertemporal Constraints
Intertemporal Constraints
Power (t=1)
Power (t=2)
Power (t=3)
Battery SOC Equation
Intertemporal Constraints
An example of
is
Intertemporal Constraints
Due to these intertemporal constraints, the optimization problem size becomes times larger, becoming more difficult to solve.

## Slide 6: Our MPOPF problem is unfortunately Nonlinear and Nonconvex – not scalable with respect to horizon duration
Model to be explained in a few slides ..
In this paper we’re interested in being able to decompose the problem with utilizing the fewest relaxations and approximations on the standard branch flow model, maintaining the fidelity of the model.

## Slide 7: Spatially Decomposing the MPOPF Problem

## Slide 8
Intuition for Spatial Decomposition
Imagine we have a bus distribution system. Substation bus is .
We wish to solve for its OPF, but would like to avoid solving the whole system in one go. Let us focus on bus .

## Slide 9
Intuition for Spatial Decomposition
Let us focus on bus .
We can see that it is one of the gateway buses between the two areas demarcated by the dashed lines.

## Slide 10
Intuition for Spatial Decomposition
We can divide the system into two areas, one where bus behaves like a load node (whose load we don’t know) and one where bus behaves as a substation node (whose voltage we do don’t know).
Now we have two OPF problems, each of half the size (and less than half the computation time) of the original problem

## Slide 11
Intuition for Spatial Decomposition
Solve OPF to get
Set
Solve OPF to get for
Set
Area
Area
Each macro-iteration (:
Are boundary variables converged?
Exchange boundary variables, and continue.
Stop
Start
Yes
No
++
Convergence means:
We call this process DOPF where D stands for Spatially Decomposed
Refer to [1] for details

## Slide 12
Intuition for Spatial Decomposition
Solve OPF to get
Set
Solve OPF to get for
Set
Area
Area
Each macro-iteration (:
Are boundary variables converged?
Exchange boundary variables, and continue.
Stop
Start
Yes
No
++
We call this process MPDOPF

## Slide 13: Modelling of our MPOPF problem

## Slide 14: Network being tested on
ENApp Approach [1]
  Divide the network into several areas to solve for their Optimal Power Flow solutions separately, with exchange of boundary variables after every ‘macro-iteration’.

## Slide 15
Modelling of Battery with Inverter
After full horizon:
Battery SOC Equation
Battery SOC Limits
Initial SOC
Terminal SOC constraint
Reactive Power
Discharging Power
Charging Power
Battery SOC
Inverter Rating
Charging/Discharging Efficiencies
Battery SOC Limits
Note: Values here are typical in OPF literature [2, 3]
Battery SOC Limits

## Slide 16
Solar PVs with Inverters
Solar Inverter Rating Limit
Reactive Power
PV Real Power
Inverter Rating
Relationships between the rated powers
Typical kW
Typically,
Typical kVAr
Typically,

## Slide 17
Network Constraints – Branch Flow Model
Bus
Bus
Load
Battery Reactive Power
Discharging Power
Charging Power
PV Reactive Power
PV Real Power
Branch
Branch
Branch
Branch Power Flow
Current Flow
Branch Power Flow
Branch Power Flow
Bus :
Bus :
Engineering Constraints
No backflow allowed
Optionally, Peak Satisfiable Demand may be specified as well

## Slide 18
Network Constraints – Branch Flow Model [1A]
Bus
Bus
Load
Battery Reactive Power
Discharging Power
Charging Power
PV Reactive Power
PV Real Power
Branch
Branch
Branch
Branch Power Flow
Current Flow
Branch Power Flow
Branch Power Flow
Bus :
Bus :
Node Real Power Balance
Node Reactive Power Balance
KVL across branch
Current Magnitude across branch
Net Generation at Node

## Slide 19
Full Optimization Model – Balanced Three-Phase Nonlinear OPF
Bus
Bus
Load
Battery Reactive Power
Discharging Power
Charging Power
PV Reactive Power
PV Real Power
Branch
Branch
Branch
Branch Power Flow
Current Flow
Branch Power Flow
Branch Power Flow
Bus :
Bus :
Desired Objective Function, (appended with an Battery Loss Function) [4]
Network Constraints
Engineering Constraints
Component Constraints (DERs, Batteries)

## Slide 20: Results and Insights

## Slide 21: Comparison between MPCOPF and MPDOPF for
Appreciable Computation Speedup (times) !
Same Converged Objective Value
Decision Variables could be different
Smaller Problem Size
Result: Proposed MPDOPF Method cuts down the computational complexity of the MPOPF problem, making way for faster solution!

## Slide 22: Checking MPDOPF Solution to see if it makes sense
Complementarity of Charging and Discharging Operations ensured despite lack of Integer Constraint Modelling
Battery Dispatch Pattern Intutively tracks the cost curve for substation power. It charges up when cost is low, and discharges (injects power into the grid) when cost if higher
Battery SOCs coming back to their original SOC values at the end of the horizon
Forecasted timeseries
Optimal Battery Actions

## Slide 23: Comparison between MPCOPF and MPDOPF for
Appreciable Computation Speedup (times) !
Same Converged Objective Value
Decision Variables could be different
Smaller Problem Size
Result: Proposed MPDOPF Method cuts down the computational complexity of the MPOPF problem, making way for faster solution!

## Slide 24: Review and Conclusion
MPOPF Problem (unrelaxed, unapproximated) can be hard to solve.
By Spatially Decomposing the system into smaller connected areas and solving for the MPOPF for each area in an iterative exchange manner, we can cut down the problem size and solving time.
But this does not truly solve the MPOPF problem, as in it also will not scale up for bigger horizon times (say, for a medium system like IEEE).
Currently we’re working on development and testing of an algorithm which will both spatially and temporally decompose the MPOPF problem, making it scalable.

## Slide 25: Thank You.

## Slide 26: Appendix and References follow

## Slide 27: References
[1] Sadnan, R., & Dubey, A. (2021). Distributed Optimization Using Reduced Network Equivalents for Radial Power Distribution Systems. IEEE Trans. Power Syst., 36(4), 3645–3656. doi: 10.1109/TPWRS.2020.3049135
[1A] Farivar, M., & Low, S. H. (2012). Branch Flow Model: Relaxations and Convexification (Parts I, II). arXiv, 1204.4865. Retrieved from https://arxiv.org/abs/1204.4865v4
[2] Eilyan Bitar's Papers. (2023, August 16). Coordinated Aggregation
of Distributed Demand-Side Resources. Retrieved from https://bitar.engineering.cornell.edu/papers.html
[3] Pandey, A., Agarwal, A., & Pileggi, L. (2020). Incremental Model Building Homotopy Approach for Solving Exact AC-Constrained Optimal Power Flow. arXiv, 2011.00587. Retrieved from https://arxiv.org/abs/2011.00587v1

## Slide 28: References
[4] Nazir, N., & Almassalkhi, M. (2021). Guaranteeing a Physically Realizable Battery Dispatch Without Charge-Discharge Complementarity Constraints. IEEE Trans. Smart Grid, 14(3), 2473–2476. doi: 10.1109/TSG.2021.3109805
[5] MultiPeriod-DistOPF-Benchmark. (2024, July 20). Retrieved from https://github.com/Realife-Brahmin/MultiPeriod-DistOPF-Benchmark