## Slide 1: Preliminary Exam Presentation
Scalable Multi-Period Optimal Power Flow for Active Distribution Systems
Aryan Ritwajeet Jha
Pursuing PhD (ECE) Power Systems

## Slide 2: Introduction and Motivation
What leads to MPOPF problem?
What’s MPOPF problem?
How to tackle it?
Intended Contributions of this PhD

## Slide 3: Introduction and Motivation
What introduces the Multi-Period Optimal Power Flow (MPOPF)? Problem?
Bus
Bus
Load
Battery Reactive Power
Discharging Power
Charging Power
PV Reactive Power
PV Real Power
Branch
Branch
Branch
Branch Power Flow
Current Flow
Branch Power Flow
Branch Power Flow
Bus :
Bus :
The distribution grid is changing due to rising penetration of Grid-Edge Devices (GEDs) such as PVs and Batteries
Eg. EVs, On-grid storage, flexible buildings
These battery devices introduce inter-temporal behaviour – their actions at one time affect future states
  This creates temporal coupling constraints
As a result, traditional OPF (single-period) is no longer sufficient
  The problem becomes Multi-Period OPF (MPOPF)
MPOPF problems are much larger (size scales with #devices x time-horizon)
  Leading to computational bottlenecks

## Slide 4: Introduction and Motivation
MPOPF Problem Visual
Bus
Bus
Load
Battery Reactive Power
Discharging Power
Charging Power
PV Reactive Power
PV Real Power
Branch
Branch
Branch
Branch Power Flow
Current Flow
Branch Power Flow
Branch Power Flow
Bus :
Bus :
Intertemporal Constraints
Intertemporal Constraints
Set Points
Intertemporal Constraints
Set Points
Set Points
Rectangle sizes representative of size of each Optimization Problem
For nonlinear optimization problems, computational burden increases superlinearly with size!

## Slide 5: Introduction and Motivation
Why Decomposition Approach?
Others have employed Successive Linearization [usmain] or Two-stage hierarchical optimization [Nawaf2018] which can miss global optimum
Realistic modelling often requires nonlinear distribution system representations
  But these are computationally expensive
Decomposition-based algorithms can break MPOPF into smaller, parallelizable subproblems
This enables:
  Scalability to larger feeders and larger timescales
  Faster or near real-time solutions
  Adoption by DSOs when GED coordination becomes operationally necessary
Accurate modelling + Scalable Decomposition is the key to enabling future grid operations

## Slide 6: Introduction and Motivation
Why Decomposition Approach? Visual
Bus
Bus
Load
Battery Reactive Power
Discharging Power
Charging Power
PV Reactive Power
PV Real Power
Branch
Branch
Branch
Branch Power Flow
Current Flow
Branch Power Flow
Branch Power Flow
Bus :
Bus :
Intertemporal Constraints
Intertemporal Constraints
Set Points
Intertemporal Constraints
Set Points
Set Points
Rectangle sizes representative of size of each Optimization Problem
Intertemporal Constraints
Intertemporal Constraints
Set Points
Intertemporal Constraints
Set Points
Set Points
For nonlinear optimization problems, computational burden increases superlinearly with size!

## Slide 7: Introduction and Motivation
Intended Contributions of my PhD
An example of
A framework for solving the MPOPF problem…
  Which has a systematic procedure to model components of power distribution system in a manner faithful to their behaviour yet computationally efficient to solve for
  That employs tailored decomposition algorithms which can exploit model’s properties to come up with an even faster solution
  Which has provision for comparison of output solution with those of trusted softwares, say OpenDSS
  Whose procedure may be theoretically justified

## Slide 8: Contents
Foundational Studies
Modelling Tradeoff Analysis
Spatial Decomposition Algorithm
Temporal Decomposition Algorithms – tADMM and DDP
Future Works

## Slide 9: Modelling Tradeoff Analysis – Linear vs Nonlinear

## Slide 10: Modelling Tradeoff Analysis – Linear vs Nonlinear
Add slides for BFM-NL vs LinDistFlow
Key Formulation Differences

## Slide 11: Modelling Tradeoff Analysis – Linear vs Nonlinear
Add slides for BFM-NL vs LinDistFlow
Key Results at a Glance

## Slide 12: MPDOPF - Spatial Decomposition of the MPOPF problem using ENApp
Intuition for Algorithm
Results

## Slide 13: MPDOPF - Spatially Decomposition MPOPF
Intuition for Spatial Decomposition
Imagine we have a bus distribution system. Substation bus is .
We wish to solve for its OPF, but would like to avoid solving the whole system in one go.
Let us focus on bus .
Source for Algorithm for OPF: ENApp [1]

## Slide 14: MPDOPF - Spatially Decomposition MPOPF
Intuition for Spatial Decomposition
Let us focus on bus .
We can see that it is one of the gateway buses between the two areas demarcated by the dashed lines.

## Slide 15: MPDOPF - Spatially Decomposition MPOPF
Intuition for Spatial Decomposition
We can divide the system into two areas, one where bus behaves like a load node (whose load we don’t know) and one where bus behaves as a substation node (whose voltage we do don’t know).
Now we have two OPF problems, each of half the size (and less than half the computation time) of the original problem

## Slide 16: MPDOPF - Spatially Decomposition MPOPF
Intuition for Spatial Decomposition via OPF (single period)
Solve OPF to get
Set
Solve OPF to get for
Set
Area
Area
Each macro-iteration (:
Are boundary variables
converged?
Exchange boundary variables, and continue.
Stop
Start
Yes
++
Convergence means:
No

## Slide 17: MPDOPF - Spatially Decomposition MPOPF
Intuition for Spatial Decomposition via OPF (single period)
Solve OPF to get
Set
Solve OPF to get for
Set
Area
Area
Each macro-iteration (:
Are boundary variables
converged?
Exchange boundary variables, and continue.
Stop
Start
Yes
++
Convergence means:
No
Add final slide showing MPOPF iterations

## Slide 18: MPDOPF - Spatially Decomposition MPOPF
Spatial Decomposition workflow for MPOPF
Solve OPF to get
Set
Solve OPF to get for
Set
Area
Area
Each macro-iteration (:
Are boundary variables
converged?
Exchange boundary variables, and continue.
Stop
Start
Yes
++
Convergence means:
No
Solve OPF to get
Set
Solve OPF to get for
Set
Area
Area
Solve OPF to get
Set
Solve OPF to get for
Set
Area
Area

## Slide 19: MPDOPF - Spatially Decomposition MPOPF
Key Results at a Glance – Scenario Setup
,
IEEE 123 1ph system with 17PVs and 26 Batteries divided into 4 Areas
NLP Problem (Not SOCP relaxed) – so somewhat slow
MATLAB fmincon+SQP

## Slide 20: MPDOPF - Spatially Decomposition MPOPF
Key Results at a Glance – Scenario Setup (Battery Modelling)
After full horizon:
Battery SOC Equation
Battery SOC Limits
Initial SOC
Terminal SOC constraint
Reactive Power
Discharging Power
Charging Power
Battery SOC
Inverter Rating
Charging/Discharging Efficiencies
Battery SOC Limits
Note: Values here are typical in OPF literature [2, 3]
Battery SOC Limits

## Slide 21: MPDOPF - Spatially Decomposition MPOPF
Key Results at a Glance – Scenario Setup (Full NLP Model)
Bus
Bus
Load
Battery Reactive Power
Discharging Power
Charging Power
PV Reactive Power
PV Real Power
Branch
Branch
Branch
Branch Power Flow
Current Flow
Branch Power Flow
Branch Power Flow
Bus :
Bus :

## Slide 22: MPDOPF - Spatially Decomposition MPOPF
Key Results at a Glance – ACOPF feasibility analyses for IEEE 123 1ph T=10
Appreciable Computation Speedup (times) !
Same Converged Objective Value
Decision Variables could be different
Smaller Problem Size
Result: Proposed MPDOPF Method cuts down the computational complexity of the MPOPF problem, making way for faster solution!

## Slide 23: MPDOPF - Spatially Decomposition MPOPF
Key Results at a Glance – ACOPF feasibility analyses for IEEE 123 1ph T=10
Simulation Scenario Slides
Optimization setup description

## Slide 24: tADMM – temporal ADMM
Formulation
Results

## Slide 25: tADMM – temporal ADMM
Consensus ADMM Schematic
Global Problem
Individual Subproblem
Individual Subproblem
Individual Subproblem
Individual Subproblem
Individual Subproblem
Individual Subproblem
Source: [ADMM notes CMU]
Consensus ADMM Formulation
Consensus ADMM Updates

## Slide 26: tADMM – temporal ADMM
Adaptation of Consensus ADMM for the MPOPF problem
Global Problem
Individual Subproblem
Individual Subproblem
Individual Subproblem
Individual Subproblem
Individual Subproblem
Individual Subproblem
Source: [ADMM notes CMU]

## Slide 27: tADMM – temporal ADMM
Algorithm formulation for copper plate example: Update 1 Primal Update
Copper Plate = 1 Substation + 1 Battery supplying 1 Load for time-steps
Input Curves:

## Slide 28: tADMM – temporal ADMM
Algorithm formulation for copper plate example: Update 1 Primal Update
Primal Updates x
Each subproblem optimizes for its non-temporal constraints only
However the temporal constraints (SOC trajectory) is computed for all time-steps
This ensures that ADMM penalty term can compare the full trajectory with the consensus
Uses last known values of and and computes

## Slide 29: tADMM – temporal ADMM
Algorithm formulation for copper plate example: Update 2 Consensus Update
Consensus Update x
Uses last known values of and and computes

## Slide 30: tADMM – temporal ADMM
Algorithm formulation for copper plate example: Update 3 Dual Update
Dual Update x
Uses last known values of and and computes

## Slide 31: tADMM – temporal ADMM
Algorithm formulation for copper plate example: Convergence Criteria
1. Primal Residual (Consensus Violation)
Each subproblem’s own copy of SOC variables should resemble that of the global copy
2. Dual Residual (Consensus Change)
The consensus value should stabilize to a fixed point
Add: Explain how adaptive ADMM is implemented!

## Slide 32: tADMM – temporal ADMM
MPOPF Simulation results for copper plate example
Battery Action plots showcase that the results (control actions for battery dispatch) are identical
Brute Forced Battery Action Plots
tADMM Battery Action Plots
All other results such as (not shown here) are also identical
Input Curves

## Slide 33: tADMM – temporal ADMM
Update modelling formulation for Full Network Model – Test Case Description
IEEE 123 1ph System with PVs and Batteries – represented in both LinDistFlow (linear) and BFM-NL (nonlinear) models
Input Curves:
IEEE123A_1ph Network

## Slide 34: tADMM – temporal ADMM
Update modelling formulation for Full Network Model – Update 1 Primal Update
Primal Updates x
This model is for LinDistFlow, but SOCP based BFM-NL has also been implemented by making the relevant adjustments (model not shown here)
Uses last known values of and and computes
Objective Function: Cost of Borrowed Substation Power + Cost of Battery Operation + Augmented Lagrangian Term

## Slide 35: tADMM – temporal ADMM
Update modelling formulation for Full Network Model – Update 1 Primal Update
Primal Updates x
This model is for LinDistFlow, but SOCP based BFM-NL has also been implemented by making the relevant adjustments (model not shown here)
Uses last known values of and and computes
specific Network Constraints: Temporally Uncoupled
Objective Function: Cost of Borrowed Substation Power + Cost of Battery Operation + Augmented Lagrangian Term

## Slide 36: tADMM – temporal ADMM
Update modelling formulation for Full Network Model – Update 1 Primal Update
Primal Updates x
This model is for LinDistFlow, but SOCP based BFM-NL has also been implemented by making the relevant adjustments (model not shown here)
Uses last known values of and and computes
specific Network Constraints: Temporally Uncoupled
Shared Temporally Coupled Constraints
Objective Function: Cost of Borrowed Substation Power + Cost of Battery Operation + Augmented Lagrangian Term

## Slide 37: tADMM – temporal ADMM
Update modelling formulation for Full Network Model – Updates 2 and 3
Consensus Updates x
Uses last known values of and and computes
Dual Updates x
Uses last known values of and and computes
Both updates are pretty much the same as that for copper plate example, only differing in having to account for multiple batteries

## Slide 38: tADMM – temporal ADMM
MPOPF Simulation results for IEEE123A_1ph – Battery Actions
These results are for nonlinear model (SOCP relaxed BFM-NL)
Battery Action plots showcase that the results (control actions for battery dispatch) are identical
Brute Forced Battery Action Plots
tADMM Battery Action Plots
Input Curves

## Slide 39: tADMM – temporal ADMM
MPOPF Simulation results for IEEE123A_1ph – PV Actions
PV Reactive Power Dispatch plots showcase are generally NOT necessarily identical
Brute Forced PV Action Plots
tADMM PV Action Plots
Input Curves
Note that PV real power dispatch is a fixed variable dependent only on (fixed variable)

## Slide 40: tADMM – temporal ADMM
MPOPF Simulation results for IEEE123A_1ph – Convergence
Convergence of Objective Function:
tADMM (Blue) vs Brute Forced (Orange)
Convergence of norms:
r-norm (Green) vs s-norm (Orange)
--- tADMM SUBPROBLEM SIZE (one time period) ---
Number of variables: 5520
Linear constraints: 8145
Quadratic constraints (SOCP): 127
Nonlinear constraints: 0
Total constraints: 8272
--- BRUTE FORCE PROBLEM SIZE ---
Number of variables: 55680
Linear constraints: 70560
Quadratic constraints (SOCP): 12192
Nonlinear constraints: 0
Total constraints: 82752

## Slide 41: tADMM – temporal ADMM
A temporal decomposition algorithm for MPOPF
Currently tADMM is converging slower than Brute-forced optimization which shouldn’t be the case since typically solution times of nonlinear problems scale superlinearly with problem size.
We feel that this might either be due to some poor optimization or some other bugs.
Currently under investigation

## Slide 42: DDP – Differential Dynamic Programming
Results

## Slide 43: DDP – Differential Dynamic Programming
Formulation for Forward Pass

## Slide 44: DDP – Differential Dynamic Programming
Currently while DDP iterations ‘hit’ near-optimal points many times, they never quite converge to a fixed point.
Key Results: IEEE123B_1ph BFM-NL with 40% PVs and 51% Batteries

## Slide 45: DDP – Differential Dynamic Programming
Key Results: IEEE123B_1ph LDF with 40% PVs and 51% Batteries

## Slide 46: DDP – Differential Dynamic Programming
Certain ‘catch convergence’ techniques were employed, but even they don’t reliably work so far.
Key Results: IEEE730_1ph LDF with 21% PVs and 31% Batteries

## Slide 47: Publications, Future Work and Timeline
Publications
Perfecting Temporal Decomposition for Medium Sized Balanced Three-Phase Systems
Temporal Decomposition for Large Sized Unbalanced Three-Phase Systems
Concluding Research and Dissertation
Timeline Gantt Chart

## Slide 48: Publications, Future Work and Timeline
Aiming to submit tADMM work as extension to the IAS paper by December 2025.
Current Publications and intended future publication
NAPS Paper
IAS Paper which can be extended to an IAS journal

## Slide 49: Future Work and Timeline
Already successfully achieved: IEEE 123 Balanced-Three Phase Network + PVs + Batteries for timesteps ( at ) solved to optimality using tADMM
But current implementation is somehow slower in time compared to brute force solution, perhaps due to poorly optimized code or other reasons – currently in investigation
Now to December 2025
Task 1: Temporal Decomposition for Medium 1ph Systems
Good convergence
Slow optimization
To fix!

## Slide 50: Future Work and Timeline
Formulate and implement tADMM for larger test systems like IEEE8500 3ph and 9500 3ph systems
  First start with LinDistFlow3ph implementation, and if successful attempt to extend to nonlinear 3ph formulation
Jan 2026 to March 2026
Task 2: Temporal Decomposition for Large Unbalanced 3ph Systems
9500 3ph System [9500Test]
Implement
IEEE 8500 3ph System [ieee8500]

## Slide 51: Future Work and Timeline
Complete investigating DDP and document its performance in a paper
Conduct a final comprehensive literature review on novel temporal decomposition methods for MPOPF
Complete any remaining implementations or case studies
Feb 2026 to May 2026
Task 3: Concluding Research and Dissertation
Try to finalize conclusion about DDP performance for MPOPF
Finish writing dissertation

## Slide 52: Future Work and Timeline
Timeline as Gantt Chart
Gantt chart showing execution plan for future works

## Slide 53: Courses
Courses (Program of Study)

## Slide 54: PhD Execution Pipeline at a Glance
Courses (Program of Study)
On track to be fulfilled by end of current semester (Fall 2025)

## Slide 55: References

## Slide 56: References
[9500Test] Introducing the 9500 Node Distribution Test System to Support Advanced Power Applications. (2023, February 03). Retrieved from https://www.pnnl.gov/publications/introducing-9500-node-distribution-test-system-support-advanced-power-applications
[ieee8500] Arritt, R. F., & Dugan, R. C. . The IEEE 8500-node test feeder. IEEE PES T&D 2010. IEEE. doi: 10.1109/TDC.2010.5484381
[1] Sadnan, R., & Dubey, A. (2021). Distributed Optimization Using Reduced Network Equivalents for Radial Power Distribution Systems. IEEE Trans. Power Syst., 36(4), 3645–3656. doi: 10.1109/TPWRS.2020.3049135
[1A] Farivar, M., & Low, S. H. (2012). Branch Flow Model: Relaxations and Convexification (Parts I, II). arXiv, 1204.4865. Retrieved from https://arxiv.org/abs/1204.4865v4
[2] Eilyan Bitar's Papers. (2023, August 16). Coordinated Aggregation
of Distributed Demand-Side Resources. Retrieved from https://bitar.engineering.cornell.edu/papers.html
[3] Pandey, A., Agarwal, A., & Pileggi, L. (2020). Incremental Model Building Homotopy Approach for Solving Exact AC-Constrained Optimal Power Flow. arXiv, 2011.00587. Retrieved from https://arxiv.org/abs/2011.00587v1

## Slide 57: References
[4] Nazir, N., & Almassalkhi, M. (2021). Guaranteeing a Physically Realizable Battery Dispatch Without Charge-Discharge Complementarity Constraints. IEEE Trans. Smart Grid, 14(3), 2473–2476. doi: 10.1109/TSG.2021.3109805
[5] MultiPeriod-DistOPF-Benchmark. (2024, July 20). Retrieved from https://github.com/Realife-Brahmin/MultiPeriod-DistOPF-Benchmark