## Slide 1
System Strength Overview
Aryan Ritwajeet Jha
Intern (Summer 2024)
Advanced System Analytics & Modelling (ASAM)
NERC

## Slide 2: System Strength [AEMO-SS-Explained]
AEMC: “System strength is a characteristic of an electrical power system that relates to the size of the change in voltage following a fault or disturbance on the power system.”
System strength is expressed in the NER by reference to fault levels while inertia to rates of change in frequency (RoCoF). They are related because inertia is critical for the power system’s resilience to changes in active power.
In spite of these similarities, their remediation is different. For example, if synchronous condensers are used to address a fault level shortfall (inject current by manipulating Q), they will provide enough fault level, but will not address an inertia shortfall (not manipulating P) unless they are coupled with a rotating mass or flywheel.

## Slide 3: System Strength [AEMO-SS-Explained]
AEMO sees system strength as the ability of the power system to maintain and control the voltage waveform at any given location in the power system, both during steady state operation and following a disturbance.
The system strength at a given location is proportional to the fault level at that location, inversely proportional to effective grid-following IBR penetration seen at that location
  (where close by grid-following IBR reduces system strength more so than electrically distant IBR).
System strength is also a function of the severity of system events on the stability of IBR
  (for example, loss of a major transmission line connecting the aforementioned location to the broader power system, resulting in sudden changes in fault level and voltage angle at that location).

## Slide 4: System Strength [AEMO-SS-Explained]
Correlations
with Available Fault Level / Short Circuit Ratio at the location
with in electrically close-by Grid Following IBRs.
Varies based on severity of system events on stability of IBR (example, loss of connecting Transmission Lines which causes change in AFL and Voltage Angle.)

## Slide 5: System Strength [AEMO-SS-Explained]
Symptoms
Wider P, V oscillations
Prolonged V recovery
Higher Transients (deeper dips, overshoots) in V
Larger step changes in V after switching capacitor/reactor banks
Increased Harmonic Distortion (by-product of low SS and higher system impedances)
Generator fault ride-through degradation (?)

## Slide 6: System Strength [AEMO-SS-Explained]
Assessments
Preliminary Assessment - SCR at point of our concern (to identify likelihood of an adverse SS impact). Compute a ‘SSQ’ (System Strength Quantity) value [AEMO-Calculating-SS] as
Full Assessment – EMT Study
  Models Used: AEMO uses PSS/E, PSCAD/EMTDC models of plants
National Electricity Rules
Hmmm, then how is SCR computed again?
There is also an value (not in NER, but in SSIAG [AEMO-SSIAG])

## Slide 7: System Strength [AEMO-SS-Explained]
Assessments
Preliminary Assessment - Interaction Factors (incorporated into the metric Short Circuit Ratio with Interaction Factors or simply SCRIF) may be accounted for depending on how many IBRs are in proximity? [Quays2023]
There are like two other (quasi steady state) metrics which I haven’t posted here.
There is also an value (not in NER, but in SSIAG [AEMO-SSIAG])

## Slide 8: AEMO Docs for TNSPs/OEMs, etc. [AEMO-SS-FAQ]

## Slide 9: AEMO Docs for TNSPs/OEMs, etc. [AEMO-SS-FAQ]

## Slide 10: System Strength [AEMO-SS-Explained]
Remedial Response (‘Do No Harm’ Policy)
I haven’t (yet) found any technical guidelines on how to plan/implement a remedial response. The reference talks about the motivation (why) but not any lower level details of the implementation (how). But it is only a starter reference.

## Slide 11
Latest Slides End. Previous Slides Follow.

## Slide 12: Objective
With the greatly expanded share of renewable in power generation, IBRs along with other components and new control schemes are being used in the modern power grid at an unprecedented scale.
Issues at various scales are being observed, which may be at least partially associated with the current implementation of IBRs [odessa22, southtexas24]
We know the symptoms, but we don’t know a systematic diagnosis. So, people have come up with the concept System Strength which will help investigate and fix these symptoms (ideally before they ever even occur).

## Slide 13: Objective
Starter questions:
How to measure system strength (SS) of a system?
What are the various kinds of issues observed when SS is low?
How to model SS with increasing complexity due to increasing number of generators in the grid?
How to provide SS through generators and inverters using new technologies?

## Slide 14: System Strength – Preliminary Definition
System Strength – AEMO understands it as the Ability of a system to maintain its Voltage (waveform and phase angle) [AEMO-SS-Brief]
How exactly (mathematically)? – A concrete metric not seen by me yet. AEMO’s guidelines have been banking on Available Fault Level (AFL).
Voltage where exactly? – Not Mathematically specified. All documents I’ve read seem to focus more on some local voltage as opposed to a particular voltage (PoI, node voltage, bus voltage, etc.)
Current ‘metric’ is basically a holistic combination of Available Fault Level and IBR Stability Criteria.

## Slide 15: System Strength - Motivation
[session01]

## Slide 16: System Strength - Classification
Babak Badrzadeh from AEMO has classified System Strength into five aspects (a ‘quincunx’ : set of five).
Each aspect itself is a trinity of approaches.
[session01]

## Slide 17: System Strength - Classification
Generation Technologies
[session01]

## Slide 18: System Strength - Classification
Analysis Types
[session01]

## Slide 19: System Strength - Classification
Timeframes
[session01]

## Slide 20: System Strength - Classification
Dispatch and Topology
[session01]

## Slide 21: System Strength - Classification
Key Enablers
[session01]

## Slide 22: System Strength - Incentivization
Proposed Market Incentivization for Injecting System Strength into the grid for GOs
[session01]

## Slide 23: Industry Example 1: GO’s ‘Do No Harm’ responsibility, PIA, FIA
[session02]
Queensland (QLD) Power Grid

## Slide 24: Industry Example 1: GO’s ‘Do No Harm’ responsibility, PIA, FIA
[session02]
Fault simulated somewhere else in the grid, and its impact on the PoI of the proposed IBR seen.
V @ PoI without SS Adverse Impact Mitigation
P, Q @ PoI without SS Adverse Impact Mitigation

## Slide 25: Industry Example 1: GO’s ‘Do No Harm’ responsibility, PIA, FIA
[session02]
V @ PoI with SS Adverse Impact Mitigation
P, Q @ PoI with SS Adverse Impact Mitigation
Fault simulated somewhere else in the grid, and its impact on the PoI of the proposed IBR seen.

## Slide 26: Industry Example 2: Harmonic Distortion due to Shunt Reactive Plant Switching
Weakness of SS causes high 5th harmonic distortion in Voltage
[session02]
Weaker grids have higher harmonic impedance, which amplify even smaller harmonic currents as a bigger harmonic voltage.
Background Harmonic Voltage – Normal Network Configuration
Fluctuation in Harmonic Voltage due to various switching in and out of shunt reactive plants
Higher Harmonics not due to any forced oscillation at the PoI, but due to background natural harmonics in the network

## Slide 27: Industry Example 2 : Harmonic Distortion due to Inverter Transformer Excitation Current
Weakness of SS causes high 5th harmonic distortion in Voltage
Harmonic Voltage Emission Limit in Harmonic of Bus Voltage is set at %
[session02]
But in reality, it is going to to !

## Slide 28: Industry Example 2 : Harmonic Distortion due to Weakened Topology
Harmonic Voltage at a weak bus shoots up when one of the connected lines is opened (network topology slightly weakened)
[session02]

## Slide 29: Industry Example 2: How to counter these Power Quality ( Harmonic) Issues?
[session02]

## Slide 30: Industry Example 4
[session02]
A: SGs along the coast
B: A + Sub-tlines (red) and Dist lines (blue)
C: B + Renewables
C: Distance between SGs and Renewables
Queensland (QLD) Power Grid
System Strength naturally diminishes with electrical distance from SGs [ARENA2020]

## Slide 31: Industry Simulation Example 3
[session02]
Later

## Slide 32: In Process: Building a Demo to demonstrate Symptoms of Weak System Strength in PSCAD

## Slide 33: In Process: Building a Demo to demonstrate Symptoms of Weak System Strength in PSCAD

## Slide 34
PV Curve
wrt changing balance point of real power at the node
Normally PV Continuation curves [PVCurve] are studied for load buses to study effect of nodal voltage due to load demand (Real) power.

## Slide 35
[ARENA2020] Managing System Strength During the Transition to Renewables. (2020, August 03). Retrieved from https://arena.gov.au/knowledge-bank/managing-system-strength-during-the-transition-to-renewables
[cigre-SS-YT-20] CIGRE Australia. (2024, June 21). AEMO/CIGRE System Strength Workshop Nov 2020. Youtube. Retrieved from https://www.youtube.com/playlist?list=PLwGHigN9C41BaJhk_rfXeoT8e67-m4aDX
[cigre-SS-Workshop-Iti]
[AEMO-SSIAG] AEMO | System Strength Impact Assessment Guidelines
[AEMO-SS-Explained] System Strength Explained (aemo.com.au)
[AEMO-SS-FAQ] System Strength Framework Frequently Asked Questions (aemo.com.au)
[AEMO-Calculating-SS] Calculating system strength quantities in the NEM (aemo.com.au)
[cigre-SS-Brief-2021] Chair, B. B. (.- C4. 5. C. a. Z. E. (.- S. C. (2021). System Strength. CIGRE. Retrieved from https://www.cigre.org/article/GB/publications/reference-papers/system-strength
References

## Slide 36
[odessa22] RSTC_Reliability_Guidelines - All Documents. (2024, June 21). Retrieved from https://www.nerc.com/comm/RSTC_Reliability_Guidelines/Forms/AllItems.aspx
[PVCurve] Contributors to Wikimedia projects. (2023, December 16). Power-voltage curve - Wikipedia. Retrieved from https://en.wikipedia.org/w/index.php?title=Power-voltage_curve&oldid=1190109767
[Quays2023] Qays, M. O., Ahmad, I., Habibi, D., Aziz, A., & Mahmoud, T. (2023). System strength shortfall challenges for renewable energy-based power systems: A review. Renewable Sustainable Energy Rev., 183, 113447. doi: 10.1016/j.rser.2023.113447
[southtexas24] South Texas Wind Events_03082024.pptx. (2024, June 21). Retrieved from https://view.officeapps.live.com/op/view.aspx?src=https%3A%2F%2Fwww.ercot.com%2Ffiles%2Fdocs%2F2024%2F03%2F06%2FSouth%2520Texas%2520Wind%2520Events_03082024.pptx&wdOrigin=BROWSELINK
References